## Slide 1: Synthetic Design Elevation [SDE] maps Methodology
Annette Grilli1, OCE
M. Spaulding1, G. Westcott1 , C. Damon2,
1 Ocean Engineering, URI
2 Environmental Data Center, URI
University OF
Rhode Island
Ocean Engineering
SDE TRAINING SESSION URI OCTOBER 24 2018

## Slide 2: FEMA’FIRM METHODOLOGY RI
HAZARD | METHOD
SURGE | EMPIRICAL BASED ON 3 TIDE GAGES EXTREME VALUE STATISTICAL ANALYSIS MEAN VALUE
WAVE | OFFSHORE : 2-D PHASE AVERAGE MODEL COASTAL + ONSHORE PROPAGATION: 1-D MODEL [WHAFIS] SELECTED TRANSECTS
EROSION | 50 m3 PROTOCOL Empirical (Hallermeier & Rhodes 1989) E =8 Tr0.4 (m3)
SDS 100-y | SURGE BASED ON EMPIRICAL DATA STEADY STATE MSL AND WAVE CLIMATE NO SEA LEVEL RISE HAZARDS ASSUMED INDEPENDENT 1-D
NEW LONDON
PROVIDENCE
NEWPORT
25 km
540 sq.ft [50 m3/m]
EROSION
University OF Rhode Island
Ocean Engineering

## Slide 3: HAZARD: STORM SURGE
HAZARD | FEMA | SDE | WHY?
SURGE | Empirical based on 3 tide gages Extreme value statistical analysis Mean value | Use of NACCS stochastic synthetic storms [Jenssen,2017] Use a suite of fully coupled surge and wave models Stochastic large number of storms Extreme value analysis based on joint probability 95% upper confidence interval | 2-D Larger pool of “possible storms” Could catch grey swans(rare event) Conservative scenario (95% CI)
WAVE |  |  | 
EROSION |  |  | 
SDS 100-y |  |  | 
University OF Rhode Island
Ocean Engineering

## Slide 4: HAZARD: WAVES
HAZARD | FEMA | SDE | WHY ?
SURGE |  |  | 
WAVE | Coastal and onshore inundation zone: 1-d model at selected transects | 2-D phase averaged model STWAVE | Continuous Coverage Includes 2-D processes [refraction]
EROSION |  |  | 
SDS 100-y |  |  | 
University OF Rhode Island
Ocean Engineering

## Slide 5: HAZARD: EROSION
HAZARD | FEMA | SDE | WHY?
SURGE |  |  | 
WAVE |  |  | 
EROSION STORM TIME SCALE | 50 m3 protocol | 2-D erosion model XBEACH | XBEACH Process based model 2-D Predicts breaching
SDS 100-y |  |  | 
University OF Rhode Island
Ocean Engineering

## Slide 6: THE 100-YEAR SYNTHETIC DESIGN STORM (SDS)
HAZARD | FEMA | SDE | WHY?
SURGE | Empirical based on 3 tide gages Extreme value statistical analysis ;Mean value |  | 
WAVE | Coastal and onshore inundation zone : 1-d model at selected transects |  | 
EROSION | 50 m3 protocol |  | 
SDS 100-y | Hazards assumed independent to estimate 1% probability of exceedance of local storm parameters Probability analysis based on past observations Steady state MSL and wave climate ; No SLR Processes in 1-D | Hazards assumed dependent (joint probability) Synthetic storms expends the range of conditions for storm generation Include SLR in projected scenario 2-D processes included | More rigorous methodology Minimize uncertainty Increase probability catching Grey Swans
University OF Rhode Island
Ocean Engineering - Grilli et al. 2018

## Slide 7: STATIC WATER LEVEL (STWL) TIDE-SURGE
DATA SOURCE
NACCS save points
MODEL
  coupled ADCIRC-STWAVE
  200 m resolution
INCLUDE
  Tide
  Wave set-up
NAACS SAVE POINTS
U.S. CORPS OF ENGINEERS
JENSEN ET AL.,2017
SURGE: “Rise in seawater during storm due to wind pushing water onshore” (NOAA)
University OF Rhode Island
Ocean Engineering -

## Slide 8: 100-Y STWL
Extreme value analysis at each save points
“100-y surge” [STWL]
Mapping across the inundation zone
Spatial variation , slope S-N ?
Balance wind/friction
Wave set-up
3
4
5
6
m
University OF Rhode Island
Ocean Engineering

## Slide 9: WAVE IN SDE
STWAVE
STeady State Spectral WAve Model (Smith, Sherlock and Resio, 1991)
2-D PHASE AVERAGE MODEL
WAVE ACTION CONSERVATION
Linear wave theory
Refraction and shoaling
Non-linear Energy Transfer due to Wave Interaction (Hasselman ;1961)
Wave breaking / Mitche criterion (depth, wave steepness)
(Battjes and Jenssen, 1978)
WAVE CREST (1%)
ASSUMING RAYLEIGH DISTRIBUTION
WC= HS*0.7*1.66
University OF Rhode Island
Ocean Engineering

## Slide 10: WAVE MODELING METHODOLOGY
COMPUTATIONAL GRID :
Discretization: 10 m
10 X 15 km
  Boundary +Initial Conditions from NACCS study
  100-year wave spectral parameters
  STWL [Tidal Surge] from NACCS 95% CI
  From coupling ADCIRC-STWAVE
  SLR linearly superimposed on STWL
3 South shore grids; 1 bay grid
Spectrum Type | Location Depth(m) | Hs (m) | Tp (s)
TMA | 43 | 7 | 20
MODEL STWAVE
University OF Rhode Island
Ocean Engineering

## Slide 11: WAVE MODELING NARRAGANSETT BAY
SOUTH WIND 35 m/s
NORTH EAST WIND 35 m/s
University OF Rhode Island
Ocean Engineering

## Slide 12: WAVE MODELING SOUTH SHORE
INUNDATION (M)
WAVE CREST (M)
University OF Rhode Island
Ocean Engineering

## Slide 13: WAVE MODELING SOUTH SHORE
ADDITIONAL ELEVATION IN WAVE CREST DUE TO DUNE EROSION
University OF Rhode Island
Ocean Engineering

## Slide 14: MODELING EVENT SCALE EROSION WITH XBEACH
XBeach (Roelvink, 2009)
Morphodynamic
Model
Wave module
Flow module
Morphology module
Sediment module
wave forcing
water level, current
sediment transport
water level, current
bed level
time
University OF Rhode Island
Ocean Engineering

## Slide 15: MODELING EVENT SCALE EROSION
XBEACH 3 MODES
STATIONARY
SURF-BEAT
NON-HYDROSTATIC
DELTARES 2018

## Slide 16: XBEACH WAVES
DELTARES 2018
DELTARES 2018
ROELVINK, 2009

## Slide 17: SOUTH SHORE BARRIER BEACHES MOVIE’ SITES
XBEACH
Surfbeat
Mode
M5
M4
M3
M2
M1
Weekapaug
Winnapaug
Charlestown
Green Hill
Matunuck
University OF Rhode Island
Ocean Engineering

## Slide 18: M1 EAST MATUNUCK 100-y STORM EROSION
University OF Rhode Island
Ocean Engineering

## Slide 19: VEGETATION EFFECT ON DUNE EROSION
VEGETATED DUNE
13 h after peak of the storm [High tide]
BARE DUNE
13 h after peak of the storm [High tide]
0
5
0
5
University OF Rhode Island
Ocean Engineering

## Slide 20: VEGETATION EFFECT ON DUNE EROSION
FEMA 20
FEMA
MODEL - VEGETATION
MODEL – BARE DUNE
 | AVERAGE ERODED VOLUME (m3/m)
FEMA | 50
MODEL VEGETATION | 46
University OF Rhode Island
Ocean Engineering

## Slide 21: EROSION SPATIAL VARIABILITY ALONG THE SHORELINE
University OF Rhode Island
Ocean Engineering
Dune crest (m) BEFORE AFTER
Bathymetry (NAVD88)

## Slide 22: CHARLESTOWN NO SLR BFE NAVD88 (m)
0 2 4 6 8 10 12 m
University OF Rhode Island
Ocean Engineering

## Slide 23: CHARLESTOWN 2ft SLR BFE NAVD88 (m)
0 2 4 6 8 10 12 m
University OF Rhode Island
Ocean Engineering

## Slide 24: CHARLESTOWN 5ft SLR BFE NAVD88 (m)
0 2 4 6 8 10 12 m
University OF Rhode Island
Ocean Engineering

## Slide 25: CHARLESTOWN 7ft SLR BFE NAVD88 (m)
0 2 4 6 8 10 12 m
University OF Rhode Island
Ocean Engineering

## Slide 26: CHARLESTOWN 10ft SLR BFE NAVD88 (m)
0 2 4 6 8 10 12 m

## Slide 27: SUMMARY METHODOLOGY SDE BFE GENERATION
Select Sea Level Rise [SLR} estimate for design life
“100-y surge” estimated from extreme value analysis at NACCS save points
XBEACH
2-d MODEL
Southern Shoreline
Large wave
Significant dune erosion
STWAVE 2-D MODEL
STWAVE 2-D MODEL
INTACT
SLR
STWL
LOCATION
Narragansett Bay
Low waves
Little erosion
NO
EROSION
DEM
WAVE
ERODED
BFE
FOR SLR SCENARIO
TOTAL STWL=SLR + STWL
NAACS WAVE SPECTRAL
PARAMETERS
LOCAL WIND
University OF Rhode Island
Ocean Engineering

## Slide 28: REFERENCES
Grilli, A., and Spaulding, M. L., Oakley, B. A. and Damon, C., 2017. Mapping the coastal risk for the next century, including sea level rise and changes in the coastline: application to Charlestown RI, USA. Natural Hazards
https://doi.org/10.1007/s11069-017-2871-x
Grilli, A.R., Spauding, M.L., Schambach, L., Smith, J. and Bryant, M., 2016. Comparing Inundation Maps Developed Using WHAFIS and STWAVE: A Case Study in Washington County, RI. Proceeding of the Coastal disaster Conference, September 9-11,2015, Boston.
https://ascelibrary.org/doi/abs/10.1061/9780784480304.016
Schambach, L., Grilli, A.R., Grilli, S., Hashemi, R., King, J., 2017. Assessing the impact of extreme storms on barrier beaches along the Atlantic coastline: Application to the southern Rhode Island coast . Coastal Engineering https://doi.org/10.1016/j.coastaleng.2017.12.004
Spaulding, M.L., Grilli, A., Damon, C., Crean, T., Fugate, G., Oakley, B.A. and Stempel, P., 2016. STORMTOOLS: coastal environmental risk index (CERI). Journal of Marine Science and Engineering, 4(3), p.54
https://doi:10.3390/jmse4030054
Wescott, W., 2018. Predicting 100-year storm wave’s runup for the coast of Rhode Island using a fully nonlinear model. Master thesis. University of Rhode Island. July 2018.
University OF Rhode Island
Ocean Engineering