## Slide 1: TRAINING ACCESS TO SDE MAPS
General access to CERI and SDE maps:
https://crc-uri.maps.arcgis.com/home/index.html
Access to SDE Narragansett Bay
https://crc-uri.maps.arcgis.com/apps/MapSeries/index.html?appid=9b85db9b7aaa400cac1a3cb404a96be8
Access to SDE South Coast
https://crc-uri.maps.arcgis.com/apps/MapSeries/index.html?appid=3ba5c4d9c0744392bec2f4afb6ee2286
Access to STORMTOOLs maps
http://www.beachsamp.org/stormtools/
REFERENCE MATERIAL at
http://www.rigis.org/data/stormtools

## Slide 2: CASE STUDY 1 NARRAGANSETT BEACH SOUTH PAVILLON
How would the Narragansett South pavillon be impacted by the “100-year” storm if it would occur today?
  Water depth, wave elevation, BFE?
If the same storm would occur in 50 years from now, how would it impact the Narragansett South pavillon?
How are these predicted water level values comparing with FEMA’s values?
Where would be the shoreline in 50 years assuming no remediation and NOAA’s high scenario?
https://crc-uri.maps.arcgis.com/apps/MapSeries/index.html?appid=9b85db9b7aaa400cac1a3cb404a96be8

## Slide 3: CASE STUDY 1 NARRAGANSETT BEACH SOUTH PAVILLON SDE - BFE
https://crc-uri.maps.arcgis.com/apps/MapSeries/index.html?appid=9b85db9b7aaa400cac1a3cb404a96be8

## Slide 4: CASE STUDY 1 NARRAGANSETT BEACH SOUTH PAVILLON SDE WAVE CREST

## Slide 5: CASE STUDY 1 NARRAGANSETT BEACH SOUTH PAVILLON SDE SURGE

## Slide 6: CASE STUDY 1 NARRAGANSETT BEACH SOUTH PAVILLON SDE WATER DEPTH

## Slide 7: SELECTING SLR SCENARIO (ft)
Sea level change calculator
https://coast.noaa.gov/digitalcoast/tools/curve.html

## Slide 8: CASE STUDY 1 NARRAGANSETT BEACH SOUTH PAVILLON SDE BFE -5 FT SLR

## Slide 9: CASE STUDY 1 NARRAGANSETT BEACH SOUTH PAVILLON SDE Wave Crest – 5 FT SLR

## Slide 10: CASE STUDY 1 NARRAGANSETT BEACH SOUTH PAVILLON FEMA BFE

## Slide 11: CASE STUDY 1 SUMMARY NARRAGANSETT BEACH SOUTH PAVILLON
Scenario | BFE [ft] | WAVE CREST [ft] | SURGE [ft] | WATER DEPTH ft] | TOPO [ft]
100-y today | 14.8 (4.5 m) | 1.8 (0.5 m) | 13 ft (4 m) | 6.6 (2 m) | 8.2 (2.5 m)
100-y 2070 NOAA High Scenario 5ft SLR | 23.4 (7.1 m) | 5.4 (1.6 m) | 13 + 5 = 18 ft (5.5 m) | 15.2 (4.6 m) | 8.2 (2.5 m)
FEMA | 15 (4.6 m) | VE ZONE |  |  | 

## Slide 12: CASE STUDY 2 CHARLESTOWN BRIDGE NINIGRET-GREEN HILL
https://crc-uri.maps.arcgis.com/apps/MapSeries/index.html?appid=9b85db9b7aaa400cac1a3cb404a96be8
How would the bridge be exposed to the “100-year storm if it would occur today?
  Water depth, wave elevation, BFE?
If the same storm would occur in 25 years from now, how would it impact the site?
Will the bridge be affected by SLR in 25 year?

## Slide 13: CASE STUDY 2 CHARLESTOWN BRIDGE NINIGRET-GREEN HILL FEMA BFE

## Slide 14: CASE STUDY 2 CHARLESTOWN BRIDGE NINIGRET-GREEN HILL SDE BFE
100 Y-STORM SURGE (95% UPPER CONFIDENCE INTERVAL) + WAVE CREST
100-Y DUNE PROFILE BASED ON XBEACH

## Slide 15: CASE STUDY 2 CHARLESTOWN BRIDGE NINIGRET-GREEN HILL SDE SURGE
100 Y-STORM SURGE (95% UPPER CONFIDENCE INTERVAL)
BASED ON NAACS DATA

## Slide 16: CASE STUDY 2 CHARLESTOWN BRIDGE NINIGRET-GREEN HILL SDE WAVE CREST
WAVE CREST = MEAN 1% HIGHEST WAVE
RESULT OF STWAVE MODEL ON HIGH RESOLUTION GRID (10 m)

## Slide 17: CASE STUDY 2 CHARLESTOWN BRIDGE NINIGRET-GREEN HILL SDE WATER DEPTH

## Slide 18: CASE STUDY 2 CHARLESTOWN BRIDGE NINIGRET-GREEN HILL SDE BFE - 2FT SLR

## Slide 19: CASE STUDY 2 CHARLESTOWN BRIDGE NINIGRET-GREEN HILL SDE WAVE CREST - 2FT SLR

## Slide 20: CASE STUDY 2 CHARLESTOWN BRIDGE NINIGRET-GREEN HILL SDE WATER DEPTH - 2FT SLR

## Slide 21: CASE STUDY 2 SUMMARY CHARLESTOWN BRIDGE NINIGRET-GREEN HILL
Scenario | BFE [ft] | WAVE CREST [ft] | SURGE [ft] | WATER DEPTH [ft] | TOPO [ft]
100-y today | 13.9 ( 4.2 m) | 0.5 ( 0.15 m) | 13.4 ( 4 m) | 7.5 ( 2.3 m) | 6.4 ( 1.9 m)
100-y in 2045 | 17.3 ( 5.3 m) | 1.9 ( 0.6 m) | 13.4+2(4.7m) | 10.9 (3.3 m) | 6.4 ( 1.9 m)
FEMA | 14 (4.3 m) | A ZONE |  |  | 

## Slide 22: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT
IS SLR AFFECTING THE VULNERABILITY OF THE SITE? How much?
IS WAVES EXPOSURE A SIGNIFICANT FACTOR IN THE SITE VULNERABILITY? What fraction of surge ?
Fields Point, RI, USA

## Slide 23: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT SDE

## Slide 24: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT WAVE CREST

## Slide 25: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT SURGE

## Slide 26: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT WATER DEPTH

## Slide 27: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT SDE - 5FT SLR

## Slide 28: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT WAVE CREST - 5 FT SLR

## Slide 29: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT WATER DEPTH - 5FT SLR

## Slide 30: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT SDE -10 FT SLR

## Slide 31: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT WAVE CREST - 10 FT SLR

## Slide 32: CASE STUDY 3 FIELDS POINT WATER TREATMENT PLANT WATER DEPTH - 10FT SLR

## Slide 33: CASE STUDY 3 SUMMARY FIELDS POINT WATER TREATMENT PLANT
Scenario | BFE [ft] | WAVE CREST [ft] | SURGE [ft] | WATER DEPTH [ft] | TOPO [ft]
100-y today | 18 ( 5.5 m) | 0.4 ( 0.1 m) | 17.6 (5.4m) | 9.2 ( 2.8 m) | 8.8 ( 2.7 m)
100-y in 2100 | 24.2 ( 7.4 m) | 1.6 ( 0.5 m) | 17.6+5 (6.9m) | 15.4 ( 4.7 m) | 8.8 ( 2.7 m)
 | 30.1 ( 9.2 m) | 2.5 ( 0.8 m) | 17.6+10(8.4m) | 21.3 ( 6.5 m) | 8.8 ( 2.7 m)
FEMA | 12 (3.7 m) | A ZONE |  |  | 

## Slide 34: Other sites
NOAA SLR viewer :
https://coast.noaa.gov/slr/
Sea level change calculator
https://coast.noaa.gov/digitalcoast/tools/curve.html