## Slide 1
STORMTOOLS Overview: Flooding, Coastal Environmental Risk Index, and Design Elevation Maps
Malcolm L. Spaulding and team*
*Annette Grilli, Chris Damon, Teresa Crean, Grover Fugate, Jim Boyd, Janet Freedman, and Reza Hashemi
Ocean Engineering, University of RI, Narragansett, RI;
STORMTOOLS Design Elevation Map
Training Sessions
Oct 24 and Nov 9, 2018

## Slide 2
STORMTOOL’s Goal: To provide access to a suite of coastal planning and design tools for coastal and riverine flooding (numerical models, maps, data sets, etc.), available as a GIS based, web service, that allows wide spread accessibly and applicability at high resolution for user selected coastal and inland areas of interest.

## Slide 3: STORMTOOLS Initiatives
Maps of flooding from sea level rise (0 to 12 ft); 25, 50, and 10o yr storms; nuisance flooding maps (1 ,2, 3, 5 and 10 yrs), flooding from historical storms (1938, Carol- 1954, Bob- 1991, and Sandy- 2012)
Development and application of Coastal Environmental Risk Index (CERI) to various communities in the state.
Development of Design Elevation Maps (SDEs) for Narragansett Bay and southern RI shoreline(South Coast).

## Slide 9: Validation with 1938, 1954, and 2012 hurricanes
Chart: Hurricane 1938
| -17.445840000000349 | -6.2227200000004945 | -5.6671200000001987 | -4.4447999999999084 | 24.446399999999812 | 34.558320000000009
STORMTOOLS | 9.6624 | 10.8125 | 10.8694 | 10.9947 | 13.9552 | 14.9914
Reported | 7.707 | 18 | 12 | 12.8 | 14.5 | 16.506 | 18.3 | 14.1 | 12.6 | 12.9 | 10.5 | 11.9 | 11.4 | 11.5 | 13.3 | 14.4 | 14.7 | 13.3 | 12.7 | 13.7 | 12.9 | 14.2 | 14.6 | 14.5 | 12.3 | 14.9 | 14.3 | 15.2 | 15 | 14.9 | 15.7 | 15.2
Chart: Carol 1954
| 1.9998266399993379 | 16.711892399999591 | 24.060702479999279 | 34.818229679999895 | 35.515396559999644 | 35.541843119999974 | 35.679631919999508
STORMTOOLS(s=1.3) | 8.9166 | 10.07 | 10.6461 | 11.4894 | 11.5441 | 11.5462 | 11.557
Reported | 8.9 | 11.1 | 13.1 | 14.4 | 13.63 | 15.22 | 10.78 | 10.1 | 9.8 | 8.9 | 9.6 | 10.1 | 10.5 | 11.1 | 13.5 | 10.1 | 11.1 | 11.8 | 12.3 | 12.5 | 14.1 | 14.2 | 12.6 | 13.9 | 13.6 | 15.3 | 13.9 | 14.4 | 14
STORMTOOLS(s=1.56) | 8.1563 | 14.5717

## Slide 10: FEMA flood zones associated water levels and waves
NAVD88
BFE
SWEL
SWEL
BFE: referenced to NAVD88
Depth of inundation,
referenced to grade elevation
Inundation depth

## Slide 11: FEMA - Flood Insurance Rate Maps (FIRMS)
Generated by FEMA for 100 and 500 yr return period surge for establishing flood insurance zones and rates. Maps expressed in terms of zones (VE, AE, and X) base flood elevation (BFE) (includes both surge and controlling wave heights).
FIRMS do not include sea level rise and hence their use to set building design standards does not accurately represent risk in the presence of sea level rise. (Their role is to determine flood zones and set flood insurance rates).
BFE maps often have serious problems (e.g. dated modeling technology, lack of consideration of uncertainty, lack of validation, subjective spatial interpolation, etc.)

## Slide 12: CERI Goal:
To develop and apply a Coastal Environmental Risk Index *(CERI) to assess the risk that structures and infrastructure face from storm surges, including flooding and the associated wave environment, in the presence of sea level rise(SLR), and shoreline erosion/accretion.
* CERI uses percent damage (or cost of damage) associated with flooding and erosion as a proxy for risk.

## Slide 13
STORMTOOLs
Storm Water Level and Waves (100 yr, with SLR)
Structures and Infrastructure
Type and Elevation
ACOE/FEMA
Wave and Inundation Damage Functions by Structure Type
STORMTOOLs Coastal Environmental Risk Index (CERI) Flow Chart
Flood/wind damage by individual structure/infrastructure
Probability distribution of damages
Damage by structure
Winds and Wind Damage Functions
BFEs

## Slide 14: CERI Building Blocks
Water levels (100 yr or specific storm event) for flooding, with or without SLR, available from STORMTOOLs. (http://www.beachsamp.org/resources/stormtools/)
Wave estimates (100 yr) for flood inundated areas, with and without SLR, based on state of the art wave models (STWAVE).
Shoreline change (erosion/accretion) estimates based on most recent 2016 RI CRMC shoreline change maps.
Damage functions by structure or infrastructure type based on data from superstorm Sandy (2012) (US Army Corp of Engineers(ACOE)/FEMA)).
Location/identification of individual structures and infrastructure from E911 and town and state data bases.

## Slide 15: Army Corp Engineers-North Atlantic Comprehensive Coastal Study (NACCS) Structure Type
5
6
7
A
B

## Slide 16: Structure Prototypes
2
3
4A
6B
Notes: Matt
Explain why we do prototypes.
To estimate damage, structures must be prototyped

## Slide 17: Structural Inundation damage by structure type

## Slide 18: NOAA Sea Level Rise (SLR) Newport, RI
CRMC SLR Guidance, NOAA High Curve (2018)
1.48 ft 2035
3.02 ft 2050
8.99 ft 2100
Year | NOAA2017 VLM | NOAA2017 Low | NOAA2017 Int-Low | NOAA2017 Intermediate | NOAA2017 Int-High | NOAA2017 High | NOAA2017 Extreme
2000 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
2010 | 0.03 | 0.16 | 0.20 | 0.30 | 0.39 | 0.46 | 0.49
2020 | 0.06 | 0.33 | 0.39 | 0.59 | 0.75 | 0.95 | 0.92
2030 | 0.10 | 0.49 | 0.59 | 0.89 | 1.21 | 1.48 | 1.57
2040 | 0.13 | 0.66 | 0.79 | 1.25 | 1.71 | 2.20 | 2.43
2050 | 0.16 | 0.82 | 1.02 | 1.64 | 2.26 | 3.02 | 3.41
2060 | 0.19 | 0.98 | 1.21 | 2.07 | 2.92 | 4.00 | 4.63
2070 | 0.23 | 1.15 | 1.41 | 2.56 | 3.64 | 5.02 | 6.00
2080 | 0.26 | 1.25 | 1.57 | 3.08 | 4.49 | 6.14 | 7.48
2090 | 0.29 | 1.38 | 1.74 | 3.64 | 5.38 | 7.55 | 9.28
2100 | 0.32 | 1.44 | 1.90 | 4.17 | 6.36 | 8.99 | 11.15
Scenarios for NEWPORT NOAA2017 VLM: 0.00322 feet/yr All values are expressed in feet
RSLC- Relative Sea Level Change

## Slide 19: Water levels Newport and Providence, RI, NOAA NOS COOPS
Newport
Providence

## Slide 20: CERI Applications *
Eastern Matunuck Beach (OCE Senior Design Class 2015-2016, Small et al, 2016)
Charlestown and Warwick, RI (HUD supported, Spaulding et al, 2016)
Misquamicut Beach, RI (OCE Senior Design Class 2016-2017)
Providence and Fox Point Hurricane Barrier (OCE Senior Design Class 2017-2018)
Barrington, Warren, and Bristol, RI (HUD supported, in progress)
STORMTOOLS Design Elevation Maps (SDE) for RI (draft maps complete). (https://crc-uri.maps.arcgis.com/home/index.html)
Waste Water Treatment Facilities (WWTF) (Fields and Bucklin Pts) and above ground storage tanks (AST) in upper Narragansett Bay (in progress, September 2018)
* http://www.beachsamp.org/stormtools/stormtools-coastal-environmental-risk-index-ceri/

## Slide 21
HUD Funded, Warwick and Charlestown, RI,
Completed, May 2017
HUD Funded, Barrington, Bristol, and Warren, RI, May 2019
OCE Seniors Design Class
Matunuck, RI, completed May 2016
Misquamicut, RI, completed May 2017
Fox Pt Hurricane Barrier, Providence, RI
completed May 2018
NOAA PSM
Southern RI shoreline, in progress

## Slide 22: Papers on STORMTOOLS and applications
http://www.beachsamp.org/stormtools/stormtools-coastal-environmental-risk-index-ceri/

## Slide 23: RI Beach SAMP Risk Based Permitting System (June 2018) * Select design life for structure/infrastructure * Determine wind and flood risk over design life (including effects of climate change, i.e. sea level rise) (STORMTOOLs Design Elevation Maps) * Assumptions of risk based on design life selected by applicant and registered on property deed.

## Slide 24: STORMTOOLs Design Elevation Maps(SDE)
BFE maps of coastal study area that explicitly include the effects of sea level rise, (used as input to CERI).
SDE maps can also be used in place of FEMA FIRMs for the design of structures and infrastructure design. ( embedded in CRMC risk based permitting system).
SDE map for the specified sea level rise value selected based on proposed design life of the structure (present date + design life = design date; sea level rise value from NOAA High Curve).
SDE maps will serve as an alternative to FEMA FIRMs, and may ultimately replace FIRMs in RI.
Freeboard offsets can be added to SDE elevations, as appropriate.

## Slide 25: SDE Maps based on upper 95% confidence limit of flooding. Why?
Large uncertainty in water levels of flooding at 100 yr return period: two major hurricanes: 1938 and 1954 dominate upper end of historical record.
Use of mean value ( 50 % confidence limit) of 100 yr inundation underestimates the risk that structures might experience in the future. See examples from recent hurricanes: Florence and Michael.
Used to address uncertainty in the analysis methodology.
Difference is consistent with impact of climate change on storm inundation. Current 95% confidence limit is consistent with 50% confidence limit considering impact of climate change on storm flooding in the future.

## Slide 26
1938
1954
Extremal Analysis
based on storm water level data at NOAA NOS stations
Large Uncertainty
2012
Storms in rank order
(relative to MHHW)
Newport, RI
1938 – 2.88 m (9.44 ft)
1954 -2.06 m (6.75 ft)
2012 -1.284 m (4.21)
1991-1.212 m (3.97 ft)
1944-1.206 m (3.95 ft)
1978 -1.1 m (3.6 ft)
1954 missing at Providence

## Slide 27: SDE Numerical Modeling Framework
Simulations of synthetic tropical (1000) and historical extratropical storms (100) using coupled ADCIRC and SWAN in ACOE North Atlantic Comprehensive Coastal Study (NACCS). Data stored at save points. Highest grid resolution (10 to 30 m).
Model system operational for RI at greatly enhanced resolution (3-5 m), Validated.
Simulation of waves in the presence of 100 yr surge and sea level rise and shoreline erosion using STWAVE.
Simulation of shoreline erosion/accretion in presence of sea level rise (XBEACH).
100 yr surge and waves, with tides, 95% confidence interval

## Slide 28
https://arcg.is/1jjbS8

## Slide 32: Summary: STORMTOOL’s SDE Maps
Objective, quantified analysis to assess flood risk using state of the art models and methods. Readily extendable to estimate damage.
Explicitly considers effects of sea level rise for various time horizons.
Assesses risk for both structures and infrastructure.
Web (publically) accessible, GIS based, downloadable, transferrable, and simple to use.
Method is consistent with building codes currently used in most states (ASCE 7-16)
Consistent with CRMC’s newly adopted risk based permitting policy.

## Slide 33
The future: CERI Risk and Damage & SDE App(start Oct 2018)
Structure Type, Design Life and Location
Site Flood Characterization
Extremal Wind Speeds
Flood Risk Maps
Flood and Wind Damage

## Slide 34: QUESTIONSS
NY Times Composite
Mexico Beach, FL; Hurricane Michael, 2018

## Slide 35: Risk maps based on SDE with SLR
Municipalities requested simplified maps that provide community leaders and the public a simple way to assess the risk of constructing a structure at any location in the town/county.
Maps must consider SLR and resulting change in sea level, erosion, and BFEs.
Method was to apply CERI and assume dominate structure
  type was at every location. Map scaled based on likely damage
  at the location: low to extreme and below MSL or eroded.

## Slide 37: Structures at risk/damaged
no SLR
2 ft SLR
5 ft SLR

## Slide 38: Overlay Structure Damage and Risk Maps (5 ft SLR)
Structure damage %
Risk Maps
Damage and risk maps overlaid

## Slide 39: STORMTOOLS Design Elevation Maps- Generation Method
Surge 100 yr return period analysis from NACCS data base
Wave heights (STWAVE)
*Offshore boundary condition from NACCS wave analysis
*Local wind forcing for bay, along central access
+
Sea Level Rise(SLR)
estimate
for design life
>
=
BFE for SLR scenario
Narragansett Bay: Low waves, little erosion
Southern RI shoreline: Large waves, significant dune erosion
Erosion/Geo-morphology Xbeach
Offshore boundary condition from NACCS
Surge 100 yr return period analysis from NACCS data base
Wave heights (STWAVE)
*Offshore boundary condition from NACCS wave analysis
*Revised digital elevation model (Xbeach)
* Local wind forcing for bay, along central access
BFE for SLR scenario
=
+
Sea Level Rise(SLR)
estimate
for design life
>
+